## Slide 1: Federation-less-federation of Network-virtualization Platforms
Yasusi Kanada, Toshiaki Tarui, and Kei Shiraishi Hitachi, Ltd.
Notes: 1

## Slide 2: Introduction
We are developing VNode and VNode Platform in a collaborative project.
VNode is a deeply-programmable physical node with network-virtualization function.
Deeply-programmable: packet data processing, such as new non-IP protocol processing, can be programmable.
VNode Platform is a virtualization platform, which enables concurrent creation and use of multiple slices (virtual networks).

## Slide 3: Research Goals
Our research goals are federation among two or more virtualization platforms including the VNode Platform.
Final goal: Heterogenious federation
  To federate new VNode Platform and several other platforms including ProtoGENI (developed in GENI Project in US).
First goal: Homogenious federation of VNode Platforms
  [Subgoal 1] To federate two or more previously-developed VNode Platforms.
    These platforms does not have federation functions.
    We intended to develop federation functions without additional development in the management system.
  [Subgoal 2] To enable Non-IP data communication on a cross-domain slice.

## Slide 4: VNode Platform and VNode
In this platform (or architecture), multiple slices can be created on one physical network.
VNode (virtualization node) is a component of the VNode platform.
  VNode is a physical node.
  VNode forwards packets on the platform as a router.
  Slices are implemented as overlay networks on the IP network.
  VNodes are connected by tunnels using GRE/IP.
    GRE (Generic Routing Encapsulation) is a protocol standardized by IETF.
(management system)
Slice specification
(IP network)

## Slide 5: Slice Creation and Management in the VNode Platform
The developer describes a slice specification.
  It specifies virtual nodes, virtual links, and binds between them.
  It is described by using an XML-based language.
  A slice is created by sending a slice specification to the domain controller (DC) of the VNode Platform.
  Other management operations, such as slice modification or deletion, is performed by using the same method.
Virtualization platform (domain)
Slice S
VN1
VN2
VN3
… N1
… N2 … N3
VL13
Slice specification
Domain controller
VNode N4
VNode N1
VN1
VN2
VN3
VNode N2
VNode N3
VL12
VL23
VL13
VL12
VL23
Operation (creation, modification, deletion, etc.)
(in XML)
(management system)

## Slide 6: Federation between Virtualization Platforms
Three categories of federation functions:
  Resource discovery functions
  Slice handling functions
  Queries on statistics and manifests
In this paper/presentation, we focus on slice handling functions, especially, slice creation.
Slice handling functions
  Functions to create and to manage a slice that spread among multiple virtualization platforms from a single platform.

## Slide 7: Federation between Virtualization Platforms (cont’d)
Basic federation method
  Instead of submitting the slice specification to both domains at once, it is passed to one domain and then passed to the other domain using the federation API.
More complicated messaging pattern
Domain A
Domain B
Slice specification
Domain C
Domain D
Federation API
Federation API
Federation API
Domain A
VNode N11
VNode
VNode N12
Domain Controller
VNode N21
VNode N22
VNode
Domain Controller
Domain B
Slice specification
VN1
VN3
VN2
VN4
VL14
VL23
Slice S
VN1
VN2
VN3
VN4
VL14
VL23
… N11
… N12 … N21
… N22
Operation (creation, modification, etc.)
Federation API (Slice Exchange Point, SEP)

## Slide 8: Conceptual Outline of Federation-less Federation
A virtualization platform without federation functions does not have a concept of “other domain”.
  The “own domain” is the only domain, or there is no “domain” concept.
The other-domain-part of the slice must belong to the own domain (for the DC).
  This means that the other domain is a sub-domain of the own domain.
  Information in the other-domain-part must be hidden from the DC in the original domain.
    Because this part is to be managed only by the DC in the other domain.
    Duplicated management of this part must be avoided.
Slice S
Own domain
Other domain
VN3
VN4
VN1
VN2
… N11
… N12
… N21
… N22

## Slide 9: Conceptual Outline of Federation-less Federation (cont’d)
PVN and DPN concepts
  In VNode Platform, the only way to express a sub-domain is to use a virtual node, which is called a pseudo virtual node (PVN).
  PVNs belong to a pseudo VNode called a domain proxy node (DPN)
Management of DPN and PVN
  DC can manage a DPN in the same way as a normal VNode.
  DC maps a PVN to a DPN by using the same way as a normal virtual node.
Slice S
Slice specification
VN1
VN2
PVN
VN3
VN4
DPN
(a pseudo VNode)
VNode N11
VNode N12

## Slide 10: Conceptual Outline of Federation-less Federation (cont’d)
DPN conceptually contains an image of the other domain.
  PVN must contain the domain-B-part of the slice specification as a sub­structure.
Federation
Domain proxy node (Subdomain)
Domain proxy node (Subdomain)
Image of the other domain
Image of own domain
Image of the other domain
Image of own domain
Domain A
Domain B

## Slide 11: Three Physical Components for Federation-less Federation
Domain proxy node (DPN)
  It receives a specification of PVN that contains the other-domain-part of slice definition and sends it to Gatekeeper.
Gatekeeper
  It receives the other-domain-part of slice definition and sends it to the other domain through the Federation API.
Gateway
  It converts the data packet from intra-domain format to inter-domain format.
The numbers of DPN, gatekeeper, and gateway may be the same or different in federation of three or more domains.
VNode N11
VNode
Domain controller
Gate-way 1
Common API
Domain D1
VNode N12
Gate-keeper 1
Domain proxy node P11
Gate-keeper 2
Federation API (control plane)
Domain D2
Data exchange (data plane)
Gate-way 2

## Slide 12: Homogenious Federation Process 1: Sender side
[Slice] In a slice specification given to DC 1, PVN encloses the other-domain-part of the slice.
  The spec is in a domain-dependent form.
[Step 2] DC 1 sends the spec to DPN, as well as normal VNodes, using the same API.
[Step 3, 4] DPN sends the spec to the other domain through Gatekeeper 1.
  Gatekeeper 1 translates the spec into a domain-independent form.
Slice S
VNode N11
VNode
DC 1
Domain D2
VNode N21
VNode
DC 2
Domain Proxy Node P21
Gate-way 1
Gate-way 2
Federation API
Slice specification S1 (domain dependent form)
VN1*
VN2*
VirtualNode PV1*
VN3*
VN4*
VL14 ††
VL23 ††
… N11**
… N12**
… N21**
… N22** … P11†
(1)
(3)
(4)
Common API
Common API
(2)
Domain D1
VNode N22
VNode N12
Gate-keeper 1
Gate-keeper 2
Domain Proxy Node P11
Operation (creation, modification, etc.)
Data exchange protocol (GRE，VLAN-based tunneling, etc.)
Domain independent form

## Slide 13: Homogenious Federation Process 2: Receiver side
[Step 5] Gatekeeper 2 sends the spec to the DC.
  Gatekeeper 2 translates the spec to domain-dependent form.
[Step 6] DC 2 sends the spec to the DPN, as well as normal VNodes, using the same API.
The spec is processed in the same method as in the sender side except Gatekeeper 2 does not send it to the sender side.
  Gatekeepers tracks the state.
VNode N11
VNode
Domain controller
Domain D2
VNode N21
VNode
Domain controller
Domain proxy node P21
Gate-way 1
Gate-way 2
Federation API
Slice S
VN3*
VN4*
VirtualNode PV2*
VN1*
VN2*
VL14††
VL23 ††
… N11**
… N12**
… P21† … N21**
… N22**
Slice specification S2 (domain dependent form)
(5)
(6)
(7)
(8)
×
Common API
Common API
Domain D1
VNode N22
VNode N12
Gate-keeper 1
Gate-keeper 2
Domain proxy node P11
GCI‡
GCI‡
Data exchange protocol (GRE，VLAN-based tunneling, etc.)
Operation (creation, modification, etc.)

## Slide 14: Homogenious federation: Notes
This method can also be applied to heterogenious federations.
  Either sender-side or receiver-side can be a different platform.

## Slide 15: Message Loop Avoidance
Inter-domain messages may cause an infinite loop because the conceptual structure is recursive.
  There may be many recursion patterns when there are three or more domains.
An Infinite loop must be avoided by using message identification and/or marking.
Domain D2
Domain Controller (DC)
Domain Proxy Node P21
Gate Keeper (GK)
Domain D1
Domain Controller (DC)
Domain Proxy Node P11
Gate Keeper (GK)
Federation
Domain proxy node (Subdomain)
Domain proxy node (Subdomain)
Image of the other domain
Image of own domain
Image of the other domain
Image of own domain
Domain A
Domain B

## Slide 16: Manageable Inter-domain Links for Non-IP Communication [Subgoal 2]
A link that corresponds to each inter-domain virtual link is created by stitching three sections.
  The inter-domain section is created through the gateway control interface (GCI) while inter-domain messaging.
  The intra-domain sections are created in the same method as normal virtual links in a domain.
The gateways may convert inter- and intra-domain protocols if necessary.
  E.g., In the current VNode Platform, GRE is used for intra-domain, VLAN is used for inter-domain.
Node N22
Gateway 2
Node N12
Gateway 1
VN1
VN4
VL14i1
conv
conv
VL14i2
VL14e
IP
MAC
IP
IP
IP
MAC
Gateway Control Interface (GCI)
Gateway Control Interface (GCI)
DPN P21
Gate-keeper 1
Gate-keeper 2
DPN P11
Federation API
Domain D1
Cross-domain network
Domain D2

## Slide 17: Issues in Federation-less-Federation Method
Restriction on modification
  If the domain does not have an operation to update a virtual node, there is no way to update the structure of the other domain.
Difficulty in collecting information
  Resource discovery, statistical query, and asking manifests* may be difficult to implement because DC does not collect information of the other domain. *manifests: virtual-node host-names or addresses, etc.

## Slide 18: Implementation and Evaluation*
An example of slice specification used for the evaluation is shown.
  Slice specification given to domain 1
    XML text
    Diagram
  Slice specification generated for domain 2

## Slide 19: Implementation and Evaluation (cont’d)*
The sequence and measured time is as follows.

## Slide 20: Conclusion
This paper proposes a method of federation between domains without a federation function.
The proposed method enables non-IP data communication on the slice.
This federation method was successfully implemented on the VNode Platform.
Future work includes heterogeneous federation, especially federation between VNode Platform and ProtoGENI.
  A limited implementation has been already demonstrated in GEC 16 (i.e., 16th GENI Engineering Conference).